## Slide 1: CS162 Operating Systems and Systems Programming Lecture 16 General I/O
March 28th, 2016
Prof. Anthony D. Joseph
http://cs162.eecs.Berkeley.edu

## Slide 2: The Requirements of I/O
So far in this course:
  We have learned how to manage CPU, memory
What about I/O?
  Without I/O, computers are useless (disembodied brains?)
  But… thousands of devices, each slightly different
    How can we standardize the interfaces to these devices?
  Devices unreliable: media failures and transmission errors
    How can we make them reliable???
  Devices unpredictable and/or slow
    How can we manage them if we don’t know what they will do or how they will perform?

## Slide 3: OS Basics: I/O
storage
Processor
OS Hardware Virtualization
Hardware
Software
Memory
Networks
Displays
Inputs
Processes
Address Spaces
Files
ISA
Windows
Sockets
OS
Threads
Protection Boundary
Ctrlr

## Slide 4: In a Picture
I/O devices you recognize are supported by I/O Controllers
Processors accesses them by reading and writing IO registers as if they were memory
  Write commands and arguments, read status and results
L3 Cache (shared)
Registers
Core
Core
Secondary Storage (Disk)
Processor
Main
Memory
(DRAM)
Registers
L1 Cache
L1 Cache
L2 Cache
L2 Cache
Secondary Storage (SSD)
I/O
Controllers
Read / Write
Read / Write
wires
interrupts
DMA transfer

## Slide 5: Operational Parameters for I/O
Data granularity: Byte vs. Block
  Some devices provide single byte at a time (e.g., keyboard)
  Others provide whole blocks (e.g., disks, networks, etc.)
Access pattern: Sequential vs. Random
  Some devices must be accessed sequentially (e.g., tape)
  Others can be accessed “randomly” (e.g., disk, cd, etc.)
    Fixed overhead to start sequential transfer (more later)
Transfer Notification: Polling vs. Interrupts
  Some devices require continual monitoring
  Others generate interrupts when they need service
Transfer Mechanism: Programmed IO and DMA

## Slide 6: Kernel Device Structure
The System Call Interface
Process
Management
Memory Management
Filesystems
Device Control
Networking
Architecture
Dependent
Code
Memory Manager
Device Control
Network Subsystem
File System Types
Block Devices
IF drivers
Concurrency, multitasking
Virtual memory
Files and dirs: the VFS
TTYs and device access
Connectivity

## Slide 7: The Goal of the I/O Subsystem
Provide Uniform Interfaces, Despite Wide Range of Different Devices
  This code works on many different devices:
  FILE fd = fopen(“/dev/something”,”rw”); for (int i = 0; i < 10; i++) { fprintf(fd,”Count %d\n”,i); } close(fd);
  Why? Because code that controls devices (“device driver”) implements standard interface
We will try to get a flavor for what is involved in actually controlling devices in rest of lecture
  Can only scratch surface!

## Slide 8: Want Standard Interfaces to Devices
Block Devices: e.g. disk drives, tape drives, DVD-ROM
  Access blocks of data
  Commands include open(), read(), write(), seek()
  Raw I/O or file-system access
  Memory-mapped file access possible
Character Devices: e.g. keyboards, mice, serial ports, some USB devices
  Single characters at a time
  Commands include get(), put()
  Libraries layered on top allow line editing
Network Devices: e.g. Ethernet, Wireless, Bluetooth
  Different enough from block/character to have own interface
  Unix and Windows include socket interface
    Separates network protocol from network operation
    Includes select() functionality
  Usage: pipes, FIFOs, streams, queues, mailboxes

## Slide 9: How Does User Deal with Timing?
Blocking Interface: “Wait”
  When request data (e.g. read() system call), put process to sleep until data is ready
  When write data (e.g. write() system call), put process to sleep until device is ready for data
Non-blocking Interface: “Don’t Wait”
  Returns quickly from read or write request with count of bytes successfully transferred
  Read may return nothing, write may write nothing
Asynchronous Interface: “Tell Me Later”
  When request data, take pointer to user’s buffer, return immediately; later kernel fills buffer and notifies user
  When send data, take pointer to user’s buffer, return immediately; later kernel takes data and notifies user

## Slide 10: Administrivia
Project 2 initial design doc due today

## Slide 11: break

## Slide 12: Chip-scale Features of Recent x86 (SandyBridge)
Significant pieces:
  Four OOO cores
    New Advanced Vector eXtensions (256-bit FP)
    Special purpose instructions: AES, Galois-Field mult
    4 -ops/cycle
  Integrated GPU, System Agent (Mem, Fast I/O)
  Shared L3 cache divided in 4 banks
  On-chip Ring bus network
    High-BW access to L3 Cache
Integrated I/O
  Integrated memory controller (IMC)
    Two independent channels of DDR3 DRAM
  High-speed PCI-Express (for Graphics cards)
  DMI Connection to SouthBridge (PCH)

## Slide 13: SandyBridge I/O: PCH
Platform Controller Hub
  Used to be “SouthBridge,” but no “NorthBridge” now
  Connected to processor with proprietary bus
    Direct Media Interface
Types of I/O on PCH:
  USB, Ethernet
  Audio, BIOS support
  More PCI Express (lower speed than on Processor)
  SATA (for Disks)
SandyBridge
System Configuration

## Slide 14: Modern I/O Systems
network

## Slide 15: Example: PCI Architecture
CPU
RAM
Memory
Bus
USB Controller
SCSI Controller
Scanner
Hard Disk
DVD ROM
Root Hub
Hub
Webcam
Mouse
Keyboard
PCI #1
PCI #0
PCI Bridge
PCI Slots
Host Bridge
ISA Bridge
ISA Controller
Legacy Devices

## Slide 16: Example Device-Transfer Rates in Mb/s (Sun Enterprise 6000)
Device Rates vary over 12 orders of magnitude !!!
  System better be able to handle this wide range
  Better not have high overhead/byte for fast devices!
  Better not waste time waiting for slow devices
10m

## Slide 17: How does the processor actually talk to the device?
CPU interacts with a Controller
  Contains a set of registers that can be read and written
  May contain memory for request queues or bit-mapped images
Regardless of the complexity of the connections and buses, processor accesses registers in two ways:
  I/O instructions: in/out instructions
    Example from the Intel architecture: out 0x21,AL
  Memory mapped I/O: load/store instructions
    Registers/memory appear in physical address space
    I/O accomplished with load and store instructions
Device
Controller
read
write
control
status
Addressable
Memory
and/or
Queues
Registers
(port 0x20)
Hardware
Controller
Memory Mapped
Region: 0x8f008020
Bus
Interface
Address+
Data
Interrupt Request
Processor Memory Bus
CPU
Regular
Memory
Interrupt
Controller
Bus
Adaptor
Bus
Adaptor
Other Devices
or Buses

## Slide 18: Example: Memory-Mapped Display Controller
Memory-Mapped:
  Hardware maps control registers and display memory into physical address space
    Addresses set by HW jumpers or at boot time
  Simply writing to display memory (also called the “frame buffer”) changes image on screen
    Addr: 0x8000F000—0x8000FFFF
  Writing graphics description to cmd queue
    Say enter a set of triangles describing some scene
    Addr: 0x80010000—0x8001FFFF
  Writing to the command register may cause on-board graphics hardware to do something
    Say render the above scene
    Addr: 0x0007F004
Can protect with address translation
Display
Memory
0x8000F000
0x80010000
Physical
Address
Space
Status
0x0007F000
Command
0x0007F004
Graphics
Command
Queue
0x80020000

## Slide 19: Transferring Data To/From Controller
addr
len
Programmed I/O:
  Each byte transferred via processor in/out or load/store
  Pro: Simple hardware, easy to program
  Con: Consumes processor cycles proportional to data size
Direct Memory Access:
  Give controller access to memory bus
  Ask it to transfer data blocks to/from memory directly
Sample interaction with DMA controller (from OSC):

## Slide 20: I/O Device Notifying the OS
The OS needs to know when:
  The I/O device has completed an operation
  The I/O operation has encountered an error
I/O Interrupt:
  Device generates an interrupt whenever it needs service
  Pro: handles unpredictable events well
  Con: interrupts relatively high overhead
Polling:
  OS periodically checks a device-specific status register
    I/O device puts completion information in status register
  Pro: low overhead
  Con: may waste many cycles on polling if infrequent or unpredictable I/O operations
Actual devices combine both polling and interrupts
  For instance – High-bandwidth network adapter:
    Interrupt for first incoming packet
    Poll for following packets until hardware queues are empty
Notes: After the OS has issued a command to the I/O device either via a special I/O instruction or by writing to a location in the I/O address space, the OS needs to be notified when:
(a) The I/O device has completed the operation.
(b) Or when the I/O device has encountered an error.
This can be accomplished in two different ways: Polling and I/O interrupt.
+1 = 58 min. (Y:38)

## Slide 21: Device Drivers
Device Driver: Device-specific code in the kernel that interacts directly with the device hardware
  Supports a standard, internal interface
  Same kernel I/O system can interact easily with different device drivers
  Special device-specific configuration supported with the ioctl() system call
Device Drivers typically divided into two pieces:
  Top half: accessed in call path from system calls
    implements a set of standard, cross-device calls like open(), close(), read(), write(), ioctl(), strategy()
    This is the kernel’s interface to the device driver
    Top half will start I/O to device, may put thread to sleep until finished
  Bottom half: run as interrupt routine
    Gets input or transfers next block of output
    May wake sleeping threads if I/O now complete

## Slide 22: Life Cycle of An I/O Request
Device Driver
Top Half
Device Driver
Bottom Half
Device
Hardware
Kernel I/O
Subsystem
User
Program

## Slide 23: Basic Performance Concepts
Response Time or Latency: Time to perform an operation(s)
Bandwidth or Throughput: Rate at which operations are performed (op/s)
  Files: mB/s, Networks: mb/s, Arithmetic: GFLOP/s
Start up or “Overhead”: time to initiate an operation
Most I/O operations are roughly linear
  Latency(n) = Overhead + n/Bandwidth

## Slide 24: Example (fast network)
Consider a gpbs link (125 MB/s)
  With a startup cost S = 1 ms
Theorem: half-power point occurs at n=S*B:
  When transfer time = startup T(S*B) = S + S*B/B

## Slide 25: Example: at 10 ms startup (like Disk)

## Slide 26: What Determines Peak BW for I/O ?
Bus Speed
  PCI-X: 1064 MB/s = 133 MHz x 64 bit (per lane)
  ULTRA WIDE SCSI: 40 MB/s
  Serial Attached SCSI & Serial ATA & IEEE 1394 (firewire) : 1.6 Gbps full duplex (200 MB/s)
  USB 3.0 – 5 gb/s
Device Transfer Bandwidth
  Rotational speed of disk
  Write / Read rate of NAND flash
  Signaling rate of network link
Whatever is the bottleneck in the path

## Slide 27: break

## Slide 28: Storage Devices
Magnetic disks
  Storage that rarely becomes corrupted
  Large capacity at low cost
  Block level random access (except for SMR – later!)
  Slow performance for random access
  Better performance for streaming access
Flash memory
  Storage that rarely becomes corrupted
  Capacity at intermediate cost (50x disk ???)
  Block level random access
  Good performance for reads; worse for random writes
  Erasure requirement in large blocks
  Wear patterns issue

## Slide 29: Are We in an Inflection Point?

## Slide 30: Hard Disk Drives (HDDs)
IBM/Hitachi Microdrive
Western Digital Drive
http://www.storagereview.com/guide/
Read/Write Head
Side View
IBM Personal Computer/AT (1986)
  30 MB hard disk - $500
  30-40ms seek time
  0.7-1 MB/s (est.)
Notes: Winchester disk drives developed by IBM: 1973 first drive
Uses “sealed” assembly with heads floating on air bearings – Bernoulli effect

## Slide 31: The Amazing Magnetic Disk
Unit of Transfer: Sector
  Ring of sectors form a track
  Stack of tracks form a cylinder
  Heads position on cylinders
Disk Tracks ~ 1µm (micron) wide
  Wavelength of light is ~ 0.5µm
  Resolution of human eye: 50µm
  100K on a typical 2.5” disk
Separated by unused guard regions
  Reduces likelihood neighboring tracks are corrupted during writes (still a small non-zero chance)

## Slide 32: The Amazing Magnetic Disk
Track length varies across disk
  Outside: More sectors per track, higher bandwidth
  Disk is organized into regions of tracks with same # of sectors/track
  Only outer half of radius is used
    Most of the disk area in the outer regions of the disk
New: Shingled Magnetic Recording (SMR)
  Overlapping tracks  greater density, restrictions on writing
  Seagate (8TB), Hitachi (10TB)

## Slide 33: Magnetic Disk Characteristic
Cylinder: all the tracks under the head at a given point on all surfaces
Read/write: three-stage process:
  Seek time: position head/arm over proper track (into proper cylinder)
  Rotational latency: wait for desired sector to rotate under R/W head
  Transfer time: transfer a block of bits (sector) under the R/W head
Disk Latency = Queuing Time + Controller time + Seek Time + Rotation Time + Xfer Time
Highest Bandwidth:
  Transfer large group of blocks sequentially from one track
Sector
Track
Cylinder
Head
Platter
Software
Queue
(Device Driver)
Hardware
Controller
Media Time
(Seek+Rot+Xfer)
Request
Result
Notes: To read write information into a sector, a movable arm containing a read/write head is located over each surface.
The term cylinder is used to refer to all the tracks under the read/write head at a given point on all surfaces.
To access data, the operating system must direct the disk through a 3-stage process.
(a) The first step is to position the arm over the proper track. This is the seek operation and the time to complete this operation is called the seek time.
(b) Once the head has reached the correct track, we must wait for the desired sector to rotate under the read/write head. This is referred to as the rotational latency.
(c) Finally, once the desired sector is under the read/write head, the data transfer can begin.
The average seek time as reported by the manufacturer is in the range of 12 ms to 20ms and is calculated as the sum of the time for all possible seeks divided by the number of possible seeks.
This number is usually on the pessimistic side because due to locality of disk reference, the actual average seek time may only be 25 to 33% of the number published.
+2 = 34 min. (Y:14)

## Slide 34: Typical Numbers for Magnetic Disk
Parameter | Info / Range
Space/Density | Space: 8TB (Seagate), 10TB (Hitachi) in 3½ inch form factor! Areal Density: ≥ 1Terabit/square inch! (SMR, Helium, …)
Average seek time | Typically 5-10 milliseconds. Depending on reference locality, actual cost may be 25-33% of this number.
Average rotational latency | Most laptop/desktop disks rotate at 3600-7200 RPM (16-8 ms/rotation). Server disks up to 15,000 RPM. Average latency is halfway around disk so 8-4 milliseconds
Controller time | Depends on controller hardware
Transfer time | Typically 50 to 100 MB/s. Depends on: Transfer size (usually a sector): 512B – 1KB per sector Rotation speed: 3600 RPM to 15000 RPM Recording density: bits per inch on a track Diameter: ranges from 1 in to 5.25 in
Cost | Drops by a factor of two every 1.5 years (or even faster). $0.03-0.07/GB in 2013
Notes: As far as rotational latency is concerned, most disks rotate at 3,600 RPM or approximately 16 ms per revolution.
Since on average, the information you desired is half way around the disk, the average rotational latency will be 8ms.
The transfer time is a function of transfer size, rotation speed, and recording density.
The typical transfer speed is 2 to 4 MB per second.
Notice that the transfer time is much faster than the rotational latency and seek time.
This is similar to the DRAM situation where the DRAM access time is much shorter than the DRAM cycle time.
***** Do anybody remember what we did to take advantage of the short access time versus cycle time? Well, we interleave!
New International Disk Drive, Equipment, and Materials Association standard is 4KB sectors instead of 512 byte sectors
+2 = 36 min. (Y:16)

## Slide 35: Disk Performance Example
Assumptions:
  Ignoring queuing and controller times for now
  Avg seek time of 5ms,
  7200RPM  Time for rotation: 60000(ms/M)/7200(rev/M) ~= 8ms
  Transfer rate of 4MByte/s, sector size of 1 Kbyte  1024 bytes/4×106 (bytes/s) = 256 × 10-6 sec  .26 ms
Read sector from random place on disk:
  Seek (5ms) + Rot. Delay (4ms) + Transfer (0.26ms)
  Approx 10ms to fetch/put data: 100 KByte/sec
Read sector from random place in same cylinder:
  Rot. Delay (4ms) + Transfer (0.26ms)
  Approx 5ms to fetch/put data: 200 KByte/sec
Read next sector on same track:
  Transfer (0.26ms): 4 MByte/sec
Key to using disk effectively (especially for file systems) is to minimize seek and rotational delays

## Slide 36: (Lots of) Intelligence in the Controller
Sectors contain sophisticated error correcting codes
  Disk head magnet has a field wider than track
  Hide corruptions due to neighboring track writes
Sector sparing
  Remap bad sectors transparently to spare sectors on the same surface
Slip sparing
  Remap all sectors (when there is a bad sector) to preserve sequential behavior
Track skewing
  Sector numbers offset from one track to the next, to allow for disk head movement for sequential ops
…

## Slide 37: Summary
I/O Devices Types:
  Many different speeds (0.1 bytes/sec to GBytes/sec)
  Different Access Patterns:
    Block Devices, Character Devices, Network Devices
  Different Access Timing:
    Blocking, Non-blocking, Asynchronous
I/O Controllers: Hardware that controls actual device
  Processor Accesses through I/O instructions, load/store to special physical memory
  Report their results through either interrupts or a status register that processor looks at occasionally (polling)
Notification mechanisms
  Interrupts
  Polling: Report results through status register that processor looks at periodically
Drivers interface to I/O devices
  Provide clean Read/Write interface to OS above
  Manipulate devices through PIO, DMA & interrupt handling
  2 types: block, character, and network

## Slide 38: Second-Chance List Algorithm (VAX/VMS)
Split memory in two: Active list (RW), SC list (Invalid)
Access pages in Active list at full speed
Otherwise, Page Fault
  Always move overflow page from end of Active list to front of Second-chance list (SC) and mark invalid
  Desired Page On SC List: move to front of Active list, mark RW
  Not on SC list: page in to front of Active list, mark RW; page out LRU victim at end of SC list
Directly
Mapped Pages
Marked: RW
List: FIFO
Second
Chance List
Marked: Invalid
List: LRU
LRU victim
Page-in
From disk
New
Active
Pages
Access
New
SC
Victims
Overflow

## Slide 39: Linux Memory Details?
Memory management in Linux considerably more complex that the previous indications
Memory Zones: physical memory categories
  ZONE_DMA: < 16MB memory, DMAable on ISA bus
  ZONE_NORMAL: 16MB  896MB (mapped at 0xC0000000)
  ZONE_HIGHMEM: Everything else (> 896MB)
Each zone has 1 freelist, 2 LRU lists (Active/Inactive)
Many different types of allocation
  SLAB allocators, per-page allocators, mapped/unmapped
Many different types of allocated memory:
  Anonymous memory (not backed by a file, heap/stack)
  Mapped memory (backed by a file)
Allocation priorities
  Is blocking allowed/etc

## Slide 40: Recall: Linux Virtual memory map
Kernel Addresses
Empty
Space
User Addresses
User
Addresses
Kernel Addresses
0x00000000
0xC0000000
0xFFFFFFFF
0x0000000000000000
0x00007FFFFFFFFFFF
0xFFFF800000000000
0xFFFFFFFFFFFFFFFF
3GB Total
128TiB
1GB
128TiB
896MB Physical
64 TiB Physical
32-Bit Virtual Address Space
64-Bit Virtual Address Space
“Canonical Hole”

## Slide 41: Virtual Map (Details)
Kernel memory not generally visible to user
  Exception: special VDSO (virtual dynamically linked shared objects) facility that maps kernel code into user space to aid in system calls (and to provide certain actual system calls such as gettimeofday()
Every physical page described by a “page” structure
  Collected together in lower physical memory
  Can be accessed in kernel virtual space
  Linked together in various “LRU” lists
For 32-bit virtual memory architectures:
  When physical memory < 896MB
    All physical memory mapped at 0xC0000000
  When physical memory >= 896MB
    Not all physical memory mapped in kernel space all the time
    Can be temporarily mapped with addresses > 0xCC000000
For 64-bit virtual memory architectures:
  All physical memory mapped above 0xFFFF800000000000

## Slide 42: Internal Interfaces: Allocating Memory
One mechanism for requesting pages: everything else on top of this mechanism:
  Allocate contiguous group of pages of size 2order bytes given the specified mask: struct page * alloc_pages(gfp_t gfp_mask, unsigned int order)
  Allocate one page: struct page * alloc_page(gfp_t gfp_mask)
  Convert page to logical address (assuming mapped): void * page_address(struct page *page)
Also routines for freeing pages
Zone allocator uses “buddy” allocator that tries to keep memory unfragmented
Allocation routines pick from proper zone, given flags

## Slide 43: Page Frame Reclaiming Algorithm (PFRA)
Several entrypoints:
  Low on Memory Reclaiming: The kernel detects a “low on memory” condition
  Hibernation reclaiming: The kernel must free memory because it is entering in the suspend-to-disk state
  Periodic reclaiming: A kernel thread is activated periodically to perform memory reclaiming, if necessary
Low on Memory reclaiming:
  Start flushing out dirty pages to disk
  Start looping over all memory nodes in the system
    try_to_free_pages()
    shrink_slab()
    pdflush kernel thread writing out dirty pages
Periodic reclaiming:
  Kswapd kernel threads: checks if number of free page frames in some zone has fallen below pages_high watermark
  Each zone keeps two LRU lists: Active and Inactive
    Each page has a last-chance algorithm with 2 count
    Active page lists moved to inactive list when they have been idle for two cycles through the list
    Pages reclaimed from Inactive list

## Slide 44: SLAB Allocator
Replacement for free-lists that are hand-coded by users
  Consolidation of all of this code under kernel control
  Efficient when objects allocated and freed frequently
Objects segregated into “caches”
  Each cache stores different type of object
  Data inside cache divided into “slabs”, which are continuous groups of pages (often only 1 page)
  Key idea: avoid memory fragmentation
Cache
SLAB
SLAB
Obj 1
Obj 2
Obj 3
Obj 5
Obj 4

## Slide 45: SLAB Allocator Details
Based on algorithm first introduced for SunOS
  Observation: amount of time required to initialize a regular object in the kernel exceeds the amount of time required to allocate and deallocate it
  Resolves around object caching
    Allocate once, keep reusing objects
Avoids memory fragmentation:
  Caching of similarly sized objects, avoid fragmentation
  Similar to custom freelist per object
Reuse of allocation
  When new object first allocated, constructor runs
  On subsequent free/reallocation, constructor does not need to be reexecuted

## Slide 46: SLAB Allocator: Cache Use
Example: task_struct_cachep = kmem_cache_create(“task_struct”, sizeof(struct task_struct), ARCH_MIN_TASKALIGN, SLAB_PANIC | SLAB_NOTRACK, NULL);
Use of example: struct task_struct *tsk; tsk = kmem_cache_alloc(task_struct_cachep, GFP_KERNEL); if (!tsk) return NULL; kmem_free(task_struct_cachep,tsk);

## Slide 47: SLAB Allocator Details (Con’t)
Caches can be later destroyed with: int kmem_cache_destroy(struct kmem_cache *cachep);
  Assuming that all objects freed
  No one ever tries to use cache again
All caches kept in global list
  Including global caches set up with objects of powers of 2 from 25 to 217
  General kernel allocation (kmalloc/kfree) uses least-fit for requested cache size
Reclamation of memory
  Caches keep sorted list of empty, partial, and full slabs
    Easy to manage – slab metadata contains reference count
    Objects within slabs linked together
  Ask individual caches for full slabs for reclamation